# General

## SUMMARY

### Provide all labor, material and equipment necessary to furnish and install aluminum windows as shown on drawings and specifications herein.  Window shapes and accessories as specified and detailed shall establish the type of units and materials to be used to provide the functional performance and aesthetic requirements desired.  Details indicate the required depth and profile.

## RELATED REQUIREMENTS

### Section 01600 – Product Requirements

### Section 07900 – Joint Sealers

### Section 08800 – Glass and Glazing

## REFERENCE STANDARDS

### AAMA/WDMA/CSA 101/I.S.2/A440-11 “Standard/Specification for Windows, Doors, and Unit Skylights”

### AAMA 502 "Voluntary Specification for Field Testing of Newly Installed Fenestration Products"

### AAMA 611 "Voluntary Specification for Anodized Architectural Aluminum"

### AAMA 701/702 "Voluntary Specification for Pile Weatherstripping and Replaceable Fenestration Weatherseals”

### AAMA 1503 “Voluntary Test Method for Thermal Transmittance and Condensation Resistance of Windows, Doors and Glazed Wall Sections”

### AAMA 2603 “Voluntary Specification, Performance Requirements and Test Procedures for Pigmented Organic Coatings on Aluminum Extrusions and Panels”

### AAMA 2604 “Voluntary Specification, Performance Requirements and Test Procedures for High Performance Organic Coatings on Aluminum Extrusions and Panels”

### AAMA 2605 “Voluntary Specification, Performance Requirements and Test Procedures for Superior Performing Organic Coatings on Aluminum Extrusions and Panels”

### ASTM E 90 “Standard Test Method for Laboratory Measurement of Airborne Sound Transmission Loss of Building Partitions”

### ASTM E 283 "Standard Test Method for Determining Rate of Air Leakage Through Exterior Windows, Curtain Walls, and Doors Under Specified Pressure Differences Across the Specimen"

### ASTM E 330 "Standard Test Method for Structural Performance of Exterior Windows, Doors, Skylights, and Curtain Walls by Uniform Static Air Pressure Difference"

### ASTM E413 “Classification for Rating Sound Insulation”

### ASTM E 547 "Standard Test Method for Water Penetration of Exterior Windows, Skylights, Doors, and Curtain Walls by Cyclic Static Air Pressure Differential"

### ASTM E966 “Standard Guide for Field Measurements of Airborne Sound Insulation of Building Facades and Facade Elements”

### ASTM E1332 “Standard Classification for Determination of Outdoor-Indoor Transmission Class”

### ASTM E1425 “Standard Practice for Determining the Acoustical Performance of Windows, Doors, Skylight, and Glazed Wall Systems”

### ASTM E1886 “Standard Test Method for Performance of Exterior Windows, Curtain Walls, Doors, and Impact Protective Systems Impacted by Missile(s) and Exposed to Cyclic Pressure Differentials”

### ASTM E1996 “Standard Specification for Performance of Exterior Windows, Curtain Walls, Doors, and Impact Protective Systems Impacted by Windborne Debris in Hurricanes”

### ASTM E 2190 "Standard Specification for Insulating Glass Unit Performance and Evaluation"

### ASTM F588 “Standard Test Methods for Measuring the Forced Entry Resistance of Window Assemblies, Excluding Glazing Impact”

### NFRC 100 “Procedure for Determining Fenestration Product U-Factors”

### NFRC 200 “Procedure for Determining Fenestration Product Solar Heat Gain Coefficient and Visible Transmittance at Normal Incidence”

### NFRC 500 “Procedure for Determining Fenestration Product Condensation Resistance Values”

## PERFORMANCE REQUIREMENTS

### Performance Requirements:  PW AW PG100

### Uniform Load Structural Test

#### With sash in a closed position window shall be tested in accordance with ASTM-E-330. At a static air pressure difference of 100.0 (150.0) pounds per square foot with pressure applied both positively and negatively.

#### Static air pressure difference shall be 1.5 times the design pressure used in 1.03 A. (1.5 is the factor used to provide a margin of safety in aluminum windows and is the minimum recommended by the AAMA).

#### At conclusion of test, there shall be no glass breakage; permanent damage to fasteners, hardware parts, support arms, or actuating mechanisms. Nor any other damage which would cause the window to be inoperable. Permanent deformation of any frame, sash, or ventilator member shall not exceed 0.04% of its span.

### Air Infiltration

#### With sash in a closed and locked position window shall be tested in accordance with ASTM-E283 and shall meet the following performance requirements.

##### Air infiltration on windows with less than 18 feet of operable sash crack perimeter shall not exceed 2.8 cfm per square foot of window area when tested in a static pressure drop of 1.57 psf (equivalent to 25 mph wind velocity) or 6.3 cfm total when tested at 6.24 psf (equivalent to 50-mph wind velocity).

##### Air infiltration on windows with 18 or more feet of operable sash crack perimeter shall not exceed .05 cfm per square foot of window area at a static pressure drop of 1.57 psf or .15 cfm at 6.24psf.

### Water Resistance

#### All tests shall be conducted in accordance with ASTM E 331. No water shall pass the innermost plane of the window when tested at a static air pressure difference of 12.0 psf.

### Thermal Performance

#### When tested in accordance with AAMA-1503 or according to NFRC-100 the thermal transmittance due to conduction (Uc) shall not exceed 0.32 on the entire specimen.

#### When tested in accordance with AAMA-1503 or according to NFRC-500 the Condensation Resistance Factor (CRF) shall not be less than 66 on the entire specimen.

### Forced Entry Resistance

#### When tested in accordance with ASTM F 588, window shall perform to a minimum Performance Level 10.

### Sound Transmission

#### Sound Transmission Class (STC).  When tested in accordance with ASTM E1425, window shall perform to a minimum STC 32 (STC 41).  Testing shall be performed in a NVLAP Certified Test Laboratory.

#### Outdoor Indoor Transmission Class (OITC).  When tested in accordance with ASTM E1332, window shall perform to a minimum of OITC 26 (OITC 33).  Testing shall be performed in a NVLAP Certified Test Laboratory.

## QUALITY ASSURANCE

### All testing shall be performed by an independent architectural testing laboratory accredited by the American Architectural Manufactures Association (AAMA), the National Voluntary Laboratory Accreditation Program (NVLAP) and the International Conference of Building Officials (ICBO) and such other accreditation as may be required by state of local building regulations.

### The manufacturer shall provide the architect and owner a notarized affidavit of compliance certifying that the doors furnished for this project are identical in every aspect of design, component parts (including sealants and the application thereof, reinforcing members, etc.) and fabrication techniques as the doors tested in the laboratory for which test reports have been furnished.

## SUBMITTALS

### Window manufacturer shall supply test reports from an AAMA- and NVLAP- accredited laboratory certifying compliance with performance specifications for each type of window supplied for this project.

### Window manufacturer shall supply product data for each type of window required, including:

#### Construction details and fabrication methods.

#### Data on hardware and accessories.

#### Recommendations for maintenance and cleaning of exterior surfaces.

### Before proceeding with the manufacture of windows, the window contractor shall submit complete shop drawings with installation details for the Architect’s approval. These drawings shall also show window elevations, details of all window sections, collateral materials, details of anchorage, associated hardware.

### Window manufacturer shall submit three [3] samples of finish.

### Window manufacturer shall submit a copy of the product warranty to be applied to this project.

## WARRANTY

### The manufacturer shall warrant the product against material defects or defects in manufacturing.  If a defect is discovered and brought to the attention of the Manufacturer, the defect will be corrected at no cost to the owner.  Warranty shall not be pro-rated.  Warranties requiring the owner to return windows to the factory for repair or replacement shall not be accepted.

#### Windows: warrant for Ten [10] years against defects in material or workmanship under normal use.

#### Insulating glass units: warrant seal for Ten [10] years against visual obstruction from film formation or moisture collection between internal glass surfaces, excluding that caused by glass breakage or abuse.

#### Finish:

##### Organic finish conforming to AAMA 2605-05: warrant for Ten [10] years against chipping, peeling, cracking, chalking, or fading.

##### Organic finish conforming to AAMA 2604-05: warrant for Five [5] years against chipping, peeling, cracking, chalking, or fading.

##### Organic finish conforming to AAMA 2603-02: warrant for One [1] year against chipping, peeling, or cracking.

# Products

## MANUFACTURER

### Basis of Design:  St. Cloud Window, Inc., 390 Industrial Blvd, Sauk Rapids, MN 56379,                   Phone: 800-383-9311, Fax: 320-255-1513, www.stcloudwindow.com

#### SCW3000 –Projecting

#### SCW3000 –Fixed Lite

### No substitutions will be accepted.

### Terminology used herein may include reference to that manufacturer’s proprietary products.  Such references shall be construed only for the purpose of establishing the quality of materials and workmanship to be applied under this section, and shall not be construed as limiting competition.

### Requests for substitutions of products or manufacturers other than the Base Bid must be submitted to the Architect Ten [10] business days prior to the bid date.  Requests for substitutions must demonstrate that the product seeking approval meets or exceeds the design and performance specifications of the Base Bid.  Products not pre-approved by the Architect in writing via addendum will not be accepted. Substitutions must comply with the requirements of section 01 60 00 – Product Requirements.

## MATERIALS

### Aluminum Extrusions

#### Shall be accurately extruded aluminum alloy 6063-T6.

#### All primary sash and frame structural members shall have a minimum wall thickness of 0.10”, unspecified wall thicknesses shall be .08”

### Insect Screen

#### All screen frames to be tubular extruded aluminum, finished with 18 x 16 screen cloth, securely held in place by means of reusable vinyl spline.  Roll-formed screen frames shall not be accepted.

#### Provide screens on operating vents as indicated on the architectural plans.

#### Flat Screens:

##### Screens shall be mounted to the interior side of frame over the operating vent. Screens will be constructed of .062 extruded aluminum.

#### Mesh to be:  Fiberglass Aluminum (Stainless Steel) (Copper)

### Thermal Barrier

#### Provide continuous extruded high performance nylon 6/6 polyamide with multi-directional 25% glass fiber reinforcing as manufactured by Technoform or equal. All polyamide material must be from a minimum of 90% virgin components, with a maximum 10% pre-consumer regrind. Aluminum components shall be mechanically crimped into cross knurled cavities and obtain a minimum composite shear value of 800 pounds for a 4” section. Rolled in PVC, single directional glass fiber reinforced polyamide and pour and de-bridge Urethane thermal break systems will not be acceptable.

### Weather-stripping

#### A rubberized vinyl EPDM weather-stripping bulb to be used in secured extruded ports at all frame vent perimeter locations.

### Hardware

#### Awning:  Concealed 4-bar stainless steel balanced arm hinges to be used at the jamb sides of vents for opening and closing operation. The frame vent will be equipped with two white bronze cam handles (a brushed nickel rotary crank style operator at the sill with a brushed nickel cam lock at each jamb) (a white bronze push-bar operator at the sill with a brushed nickel cam lock at each jamb)  to hold the vent in a tightly closed and locked position.

#### Casement:  Exposed knuckle hinges located at the jamb and finished to match the window frame (Concealed 4-bar stainless steel balanced arm hinges to be used at the head and sill of vents for opening and closing operation). The frame vent will be equipped with a brushed nickel rotary crank style operator at the sill with two brushed nickel cam locks at the jambs (white bronze cam handle at the jamb) (brushed nickel pull handle with a concealed friction arm and two brushed nickel cam locks at the jamb) (white bronze push-bar operator at the sill with a brushed nickel cam lock at each jambs) to hold the vent in a tightly closed and locked position.

#### Hopper:  Concealed 4-bar stainless steel balanced arm hinges to be used at the jamb sides of vents for opening and closing operation. The frame vent will be equipped with two white bronze cam handles to hold the vent in a tightly closed and locked position. Hardware to accept pole operators at window locations as indicated on the architectural drawings.

### Glazing

#### All glazing shall comply with the performance requirements outlined in section 08800 – Glass and Glazing.

#### All windows to be fully factory glazed with 1” 1.25” 1.50” thick overall insulated glass.

#### All glass shall be glazed with removable stops and shall be replaceable without dismantling the sash or frame members.

#### A continuous polyshim tape will be used on the exterior glazing leg and a continuous silicone cap bead over the polyshim bonding to the glass edge to prevent moisture from intruding into the window system.  A continuous rubberized vinyl compression bulb to be used on the interior glazing stops.

#### Nominal glass thickness and type shall be:

##### Exterior glass lite

###### Thickness: 1/4"

###### Tint:  clear (bronze) (gray) (green) (blue)

###### Type:  annealed (tempered) (laminated)

###### Coating:  none (Cardinal 272 LowE) (Cardinal 366 LowE)

##### Air Space

###### 1/2” (Air Filled) (90% Argon Filled)

##### Interior Glass Lite

###### Thickness:  1/4"

###### Tint:  clear (pattern #62 obscure)

###### Type:  annealed (tempered) (laminated)

###### Coating:  none (Cardinal i89 on #4 surface)

### Muntin:

#### Muntin grids shall be extruded aluminum with exposed surfaces finished to match window exterior and interior colors

#### Muntin grids shall be applied to the interior and exterior of the glass lite to simulate a true-divided lite.

#### Insulated glass units shall incorporate between glass grids to simulate a true-divided lite.

#### Grid patterns to be designated by architect.

### Strap Anchors:

#### A continuous aluminum slip-on F-channel mounting clip will be used on the interior side of window frame perimeter to anchor window frames in place. A fastener will be anchored through mounting clip into the wall section 6” from each frame edge and at 16” on center or a determined spacing as set forth by engineered load calculations. After fasteners are in place, a trim cover plate will be snapped over the mounting clip to conceal all fasteners.

## 2.03	FABRICATION

### All joints of the frame shall be butt type and secured by means of thread-cutting  stainless steel screws anchored into screw ports which shall be an integral part of the frame members. The vent frame shall use miter-type joinery and be secured together with the use of aluminum corner keys and crimped. All corner joints shall be joined neatly and all sharp edges shall be de-burred and filed smooth. Joints to be sealed for weather tightness with the use of small joint sealer material.

## 2.04	FINISH

### Interior:  (Choose only one of the following and delete all remaining verbiage including this note).

#### Anodized Finish:  Class II (etched and anodized to 0.4 mil), conforming to AAMA 611-98

##### Color to be Clear

#### Anodized Finish:  Class I (etched and anodized to 0.7 mil), conforming to AAMA 611-98

##### Color to be: Clear, Black, Dark Bronze, Med. Bronze, Lt. Bronze, Champagne

#### Polyvinylelidene Fluoride PVDF Organic Coatings:   Finish shall be 70% fluoropolymer (PVDF) organic coating in a color selected by Architect. Applied coatings shall meet or exceed AAMA 2605-05, including 10 years Florida exposure and 4000 hours humidity tests.

##### Color to be:

#### Polyvinylelidene Fluoride PVDF Organic Coatings:  Finish shall be 50% fluoropolymer (PVDF) organic coating in a color selected by Architect.  Applied coatings shall meet or exceed AAMA 2604 -05, including 5 years Florida exposure and 3000 hours humidity tests.

##### Color to be:

#### Pigmented Organic Coatings:  Finish shall be Baked Enamel organic coating in a color selected by Architect.  Applied coatings shall meet or exceed AAMA 2603 -02, including 1 year Florida exposure and 1500 hours humidity tests.

##### Color to be:

### Exterior:  (Choose only one of the following and delete all remaining verbiage including this note)

#### Anodized Finish:  Class II (etched and anodized to 0.4 mil), conforming to AAMA 611-98

##### Color to be Clear

#### Anodized Finish:  Class I (etched and anodized to 0.7 mil), conforming to AAMA 611-98

##### Color to be: Clear, Black, Dark Bronze, Med. Bronze, Lt. Bronze, Champagne

#### Polyvinylelidene Fluoride PVDF Organic Coatings:   Finish shall be 70% fluoropolymer (PVDF) organic coating in a color selected by Architect. Applied coatings shall meet or exceed AAMA 2605-05, including 10 years Florida exposure and 4000 hours humidity tests.

##### Color to be:

#### Polyvinylelidene Fluoride PVDF Organic Coatings:  Finish shall be 50% fluoropolymer (PVDF) organic coating in a color selected by Architect.  Applied coatings shall meet or exceed AAMA 2604 -05, including 5 years Florida exposure and 3000 hours humidity tests

##### Color to be:

#### Pigmented Organic Coatings:  Finish shall be Baked Enamel organic coating in a color selected by Architect.  Applied coatings shall meet or exceed AAMA 2603 -02, including 1 year Florida exposure and 1500 hours humidity tests.

##### Color to be:

# 2.05	Erection

## INSTALLATION

### All window and related window components shall be installed in accordance with requirements of the owner and the approved shop drawings of the Manufacturer.  Installation shall be by a contractor who is experienced and who shall document at least one other projects of similar nature and scope for which the window products were successfully installed.

### All materials shall be erected plumb, level and true, relative to the building structure.  The maximum variation from plumb and level shall not exceed 1/8” (plus or minus) over ten feet.

### Approved insulation materials shall be installed in the frame cavity on the interior portion of the window frame.  Area adjacent to the exterior of the window frame shall remain uninsulated.  The window installer shall use caution in the insulation operation to avoid overlapping insulation materials across the thermal-barrier connector thus bridging the two separate frame members.

## CAULKING

### A grade “A” type neutral cure silicone caulking:  Pecora, Tremco, Vulkem, or equal as approved by the Architect, shall be applied per the installation drawings and details at all points where the aluminum master frame and/or panning intersects the masonry or other exterior wall finish.  The caulking material shall be applied in a manner which insures a continuous air- and water-tight perimeter seal.  Color to match the color of the aluminum windows unless specified otherwise by the Architect.

## TESTING

### Laboratory Testing

#### At the discretion of the owner, one or a number of window units shall be selected prior to installation. The selected stock shall be tested by a certified testing laboratory to verify that glass, glazing, hardware and finish are in conformance to the project specification. Should any component of the test specimen fail to conform to project specification, action shall be taken by the window manufacture to correct each deficiency for every window on the project at no additional cost to the owner

#### The owner shall assume the cost of the initial verification testing. However, should product be found to be non-compliant, the manufacture shall reimburse the owner for the cost of the initial test. At the architect’s discretion, subsequent testing may be required and the cost of this test shall be borne by the manufacture.

### Field Testing

#### On-site testing shall be conducted at owner’s discretion and expense. Up to three test specimens shall be selected by owner or architect.

#### On-site testing shall be conducted for air infiltration and water leakage as specified in section 1.04 – A and b, by an AAMA-certified architectural testing laboratory in accordance with AAMA 502, Method B.

#### On-site testing shall be conducted for sound transmission as specified in section 1.04 – F and G, by NAVLAP-certified acoustic testing laboratory in accordance with ASTM E966 and including flanking test. Using ASTM E413 and ASTM E1332, respectively, specimens tested in the field shall be within five (5) points of the laboratory STC test results and three (3) points of the laboratory OITC test results furnished with product qualification.

#### If a test specimen shall fail any aspect of the field test, it shall be repaired or replaced and re-tested. At the architect’s direction, up to three (3) additional windows may be tested. Upon completion of re-testing, all window units shall be repaired or replaced in the same manner as the test specimen (s) to assure compliance with project performance specification.

#### The cost of re-testing and all subsequent repairs and other associated expenses shall be borne by the window manufacture and/or window installation contractor

## ADJUSTMENTS, PROTECTION, AND CLEANING

### After installation, the erector shall remove all sealants, caulking and other misplaced materials from all surfaces, including adjacent work. The window frame, sash and glass shall be cleaned thoroughly with materials and methods recommended by the window and glass manufacturers and shall not cause any defacement of the work.

### Installer shall make any and all adjustments to window sash and hardware to cause the operating sash to function properly and in accordance with the manufactures standards

### Protection of glass and window materials: Protect from contact with contaminating substances resulting from construction operations. After installation and cleaning of windows by window contractor, the general contractor shall be responsible for maintaining the cleanliness and protection of the window from damage from other trades.

### Remove all sealant, caulking and other misplaced materials from all surfaces, including adjacent work. The window frames, casing, and glass shall be thoroughly cleaned with materials and methods recommended by the window and glass manufacturer and shall not cause any defacement of the work.

### The general contractor shall be responsible for the protection of the work from damage by other trades.